## Slide 1: Lockout/tagout for authorized employee
OSHA’s Control of Hazardous Energy
29 CFR 1910.147
29 CFR 1910.133
Administered by
Skidmore College

## Slide 2: Objectives
  Recognize hazardous energy sources
  Understand responsibilities to create and maintain safe conditions
  Control hazardous energy with lockout/tagout

## Slide 3: What is hazardous energy?
How can you protect yourself without knowing what the hazardous energy sources you may encounter?

## Slide 4: What is hazardous energy?
  Often invisible
  Can be hydraulic or mechanical
  Live or stored
  Moving machine or equipment parts

## Slide 5: Examples of hazardous energy
  Thermal
  The force of GRAVITY that could cause machinery to continue to move

## Slide 6: Examples of hazardous energy
  Electricity, where the flow of electrical current can cause an unsafe condition;
  Pressure of fluids or air, as with pneumatic or hydraulic equipment;

## Slide 7: Examples of hazardous energy
  Steam, such as when it remains in a pipe after shutoff; and
  Chemicals

## Slide 8: Hazardous energy injuries
  Thousands of injuries each year
  80% of workers fail to turn off equipment
  Causes:
    Unexpected start-up
    Release of stored energy
    Failure to lockout/tagout

## Slide 9: Controlling hazardous energy
  Follow lockout and tagout procedures
  Prevent machinery or equipment from being turned on
  Dissipate energy
  Prevent a part of machinery or equipment from moving
  Provide means of warning (tag)

## Slide 10: Lockout tagout regulations
29 CFR 1910.147
  “Authorized employee” who services machinery
  “Affected employee” who operates machinery
  “Other employee” near machinery and equipment

## Slide 11: Authorized employee
  Trained to perform locking or tagging procedures
  No other employee can attach or remove lock or tag devices

## Slide 12: Authorized employee
  Responsibilities
  Repair or service equipment as needed
  Ensure that all energy sources are locked out
  Test equipment to verify residual energy is dissipated
  Place tags on equipment

## Slide 13: Authorized employee
  Responsibilities (cont’d)
  Obtain assistance when necessary
  Remove locks and/or tags following lockout/tagout
  Coordinate multishift repair

## Slide 14: Affected employee
  Operates machinery or equipment
  Aware of energy control procedures
  Performs emergency procedures
  Affected employees MUST understand what Lockout/Tagout is

## Slide 15: Affected employee
  Responsibilities
  Notify maintenance
  Leave all lockout/ tagout devices in place
  Verify equipment is safe to operate
  Ensure safety guards are in place and functioning
  Follow all safety rules

## Slide 16: Workplace responsibilities
Ensure de-energization of equipment
Ensure employee awareness
Provide appropriate levels of training
Review program effectiveness
Maintain and revise program
Administer appropriate disciplinary actions

## Slide 17: exercise
Authorized Employee
Affected Employee
Repair equipment
Place tags on equipment
Verify equipment is safe to operate
Remove locks or tags
Test equipment
Notify maintenance for servicing
Test equipment

## Slide 18: Recognize and control hazardous energy
Do you understand how to recognize and control hazardous energy?

## Slide 19: Energy isolation device
  Isolate the equipment from the energy source
  Isolation device
        Circuit breaker
        Pressure valve
        Machine block

## Slide 20: Lockout device
    Lock
    Block
    Chain
    Multilock hasp
    Wheel valve cover
    Ball valve cover

## Slide 21: Tagout device
  Warning devices only
  Legible
  Attached securely
  Resistant to degradation
  Removed only by an authorized employee

## Slide 22: Requirements for lockout/tagout devices
  Durable
  Standardized
  Traceable
  Substantial
  Identifiable

## Slide 23: Typical equipment requiring lockout/tagout
Fan motors
Light fixtures
Water Valves
Table Saws
Hydraulic Hoses
Air Handlers
Automobiles/Trucks
WHAT ELSE?

## Slide 24: When to use lockout/tagout devices
Use lockout/tagout when:
  Equipment needs servicing
  Hazardous energy exists
  Unexpected start-up could occur

## Slide 25: Actions that trigger LOTO
  Removing or bypassing a safety device
  Any part of the body is placed in harm’s way
  Exposure to hazardous energy

## Slide 26: Loto exceptions
  When hazardous energy does not exist
  During routine production processes
  Cord-controlled devices
  Hot tap operations

## Slide 27: Lockout/tagout procedure
Preparation: review all hazards and controls and perform full employee briefing.
Notify affected personnel, verify it is safe to shut down the equipment.
Isolate energy sources - perform normal equipment shutdown.
Apply LOTO Device - Lock and Tag
Release Stored Energy if necessary (apply blocks, grounds, etc.)
Test and Restart to Verify Zero-Energy State - RETURN OPERATING CONTROL(S) TO "NEUTRAL" OR "OFF" POSITION AFTER THE TEST.

## Slide 28: Restart procedure
Clean up and inspect equipment. Ensure no tools or materials are left in or around the equipment.
Clear affected personnel away from area to ensure that no one is exposed.
Verify that the controls are in neutral.
Remove Locks and Tags.
Reactivate isolation device(s) to restore energy to the equipment.
Notify the "affected" employees of their removal and startup.
You are now ready to restart machinery or equipment.

## Slide 29: Exercise – what steps should you take to perform a proper loto?
Put the steps in their proper order:
Notify affected personnel
Apply LOTO Device - Lock and Tag
Test and Restart to Verify Zero-Energy State
Preparation: review all hazards and controls
Isolate energy sources - perform normal equipment shutdown.
Release Stored Energy if necessary (apply blocks, grounds, etc.)
1.
2.
3.
4.
5.
6.

## Slide 30: Loto device and procedures
Do you understand:
  How to recognize hazardous energy?
  When you must use LOTO?
  All lockout/tagout procedures for controlling hazardous energy?

## Slide 31: Key points to remember
  Energy can be dangerous and deadly
  When in doubt, lock it out!
  Adhere to lockout/tagout and restart procedures
  Keep everyone informed